Annex 1

MAURITIUS  PORTS  AUTHORITY

DETAIL OF TUG

The general particulars of the Voith Tractor Tug are as follows:-

Year Built: 1987

Shipyard: Messrs Martin Jansen Shipyard

Country of origin : Germany

Principal Dimensions: Length Overall 29.25 m

Breadth Overall 9.64 m

Depth to Main Deck 3.61 m

Harbour Service Draft 4.4 m

Bollard Pull: 30 Tonnes

Speed: 11.8 Knots

Main Engines: Two KHD – SBV 6 m 628

Marine Diesel Engines 1000 kw each

Propulsion: Two Voith Controllable Pitch Propellers, Type VSP 26 G 11

Auxilliary Diesel Engines: Two MWM – TD 226-6 (80 KW each)

Main Engine Driven Fire Fighting Pumps: 2 x 360 m3/h

Fresh Water Capacity:25m3

Classification: Bureau Veritas

Electrical System: 400 V AC/ 220 V AC/ 3 Phase/ 50 Hz/ 24 V DC

Towing Winch: One Aft–Safe Working Load 35 Tonnes Brake Holding Load: 70 Tonnes

Towing Hook: One Aft– Safe Working Load 35 Tonnes Test Load: 70 Tonnes Make: Wieckhoff

Gross Tonnage: 254.17 T Net Tonnage: 85.92T

Fuel Capacity: 110 m3 Light Diesel Oil

Accommodation: 10 persons